## Slide 1: Mobile GPU approaches to power efficiency
Andrew Gruber
  VP, Technology
  Qualcomm Technologies, Inc.
July 2019

## Slide 2: Overview
What is the typical mobile environment?
Rendering algorithm differences with desktop
Performance and perf/watt comparison with desktop
Physical design and power management
Notes: Convince you that mobile GPUs are real GPUs and that they have a significant perf/watt advantage over laptop and desktop parts.

## Slide 3: Mobile Memory Systems
Architecture
  Desktop GPUs have dedicated DDR
    Typically GDDR used for higher end GPUs
  Mobile GPUs share DDR with other IPs
    LPDDR used for Mobile SOCs
    Mobile GPU typically given low priority (higher latency) compared to other real-time IP’s (Camera/Modem) on the SOC
Performance/Power
  LPDDR has less than half BW per pin compared to GDDR
  LPDDR ~10% more power efficient than GDDR at peak freq
    Larger benefit for LPDDR exists at lower frequencies
Product | Class | Tier | BW (GB/s) | Capacity (GB)
Nvidia 2080 Ti | Desktop | High | 616 | 11
Nvidia 1050 | Desktop | Low | 112 | 2
Galaxy S10 | Mobile | High | 33 | 8
Nokia 8810 4g | Mobile | Low | 4 | 0.5
Chart: Performance [Gbps/pin]
| 2015 | 2016 | 2017 | 2018 | 2019
GDDR | 7 | 10 | 14
LPDDR | 3.25 | 4 | 6.5
DDR | 2.5 | 3 | 4
Chart: Power Efficiency [mW/GBps]
| 2015 | 2015.5 | 2016 | 2017 | 2018 | 2019
GDDR | 1 | 0.47 | 0.32
LPDDR | 0.8 | 0.5 | 0.4 | 0.25
DDR | 0.98 | 0.62 | 0.46
Memory technology trend
  GDDR6 with over 14Gbps, beyond 10Gbps GDDR5
  LP5, 20% more power-efficient than LP4X
Notes: Bandwidth roughly 20x – while capacity is more competitive. Bandwidth made up later.
LP DDR has lower bandwidth but more power efficient especially compared to DDR ‘system memory’ alternatives

## Slide 4: Mobile GPU, APIs and other trends
In terms of APIs, recent mobile GPUs are on parity with Desktop parts
  DX12 and Vulkan are widely supported including shaders required for Tesselation
New features such as Variable Rate Shading and WaveMath will rapidly migrate to Mobile
As new rendering techniques (Ray Tracing/Mesh Shading) gain traction in the Desktop space, they may migrate to mobile.
Power saving features (Render Target Compression, FP16 math ops, ASTC, Vulkan Subpasses) show up first – even prior to Desktops.
Gaming capability is rapidly approaching previous Generation consoles. The Qualcomm® SnapdragonTM 855 mobile platform in Galaxy S10 has 954 GFLOPS of Shader performance vs. 1300 GFLOPS in the Xbox-One.
Mobile SoCs are widely used in VR applications and have support for View Instancing
Mobile GPUs do support OpenCL compute and machine learning, often with some specialized 8 bit integer instructions. Within the mobile SOC it is common to have dedicated ‘AI’ cores as well.
Specs | Qualcomm® AdrenoTM 640 GPU | Xbox One
Shader ALU (FP32) | 954.7 GFLOPs | 1300 GFLOPs
Shader ALU (FP16) | 1853.3 GFLOPs | 1300 GFLOPs
Texture (Bilinear) | 28.1 Gtex/sec | 40.9 Gtex/sec
ROPs | 9.4 Gpix/sec | 13.6 Gpix/sec
System/Tile Memory Bandwidth | 34.1 GB/sec 300 GB/sec | 68 GB/sec 200 GB/sec
Qualcomm Snapdragon and Qualcomm Adreno are products of Qualcomm Technologies, Inc. and/or its subsidiaries
Notes: Show comparable numbers -- even better for FP16. These are real Gigaflops (Shader code). No isolated Interpolator or Addressing Unit. IEEE compliant.

## Slide 5: Power Consumption within a Mobile GPU
GPU and Memory power are about as dominant power consumers
  CPU power consumption is less, but still significant
  PMIC (Power Management IC [voltage regulator]) can also burn significant power
API chosen and driver maturity can have a large effect on overall power consumption
  Vulkan based application’s power consumption is lower on the CPU than with OpenGL ES
Chart: Game Power distribution on Snapdragon SoC
| CPU | GPU | Memory | PMIC

 | 0.16708 | 0.32477 | 0.30252 | 0.20564
Note: Silicon based measurement of Fortnite
Notes: Memory is a large consumer despite caching, compression and LP-DDR usage.

## Slide 6: Rendering algorithm differences with desktop GPUs
Mobile chips typically use some form of ‘Binned’ rendering into an on-chip tile buffer
There is commonly a separate ‘Binning Pass’ that generates visibility information that is used for later ‘Rendering Pass’. Intel calls this pass ‘POSH’ – position only shading – as only position information is required.
Finally the results are copied to the system memory surface in a ‘resolve pass’. Note that surfaces that are no longer needed (such as depth) are not resolved and any traffic associated with them stays on-chip.
AdrenoTM GPU supports Direct Rendering as well (we call this ‘Qualcomm® FlexRenderTM Technology’) for situations in which the depth complexity is low and not worth the binning and resolve overhead. In these cases, some of the tile buffer is used as system memory cache.
Qualcomm Adreno and FlexRender is a product of Qualcomm Technologies, Inc. and/or its subsidiaries
Binning Pass
Resolve Pass
Rendering Pass
Binning Pass for next frame
GPU hw creates Visibility Streams*
Primitives
0
1
1
1
0
1
0
0
11
Bin#1
00
Bin#2
01
01
Etc…
Streamers Data
Setup Visibility Stream based on Frame Buffer size
RLE of Visibility Streams are written to system memory
Z-test, Alpha-test Fragment Shading, Blending of layers
Rasterization of Primitives
Execute draw calls per bin using current bin’s Visibility Stream
Render First Bin
Render Next Bin
Rendering Pass Initiated
Transform Primitive Positions
Write final color values from GMEM tile to the frame buffer in system memory
If last bin in the current frame, the driver swaps buffers, and starts rendering the first bi from next frame
Write color and z for all pixels in the current bin to internal the “GMEM” tile buffer (e.g. GMEM = 1MB for A330/8974)
Notes: Some mobile architectures do it a little differently – by doing the complete Vertex Shading during the binning pass and saving out the transformed Vertex. This is a tradeoff of VS cycles vs additional memory bandwidth/complexity.
The Binning Pass may concurrent (i.e. for the following frame) in some architectures. Similarly ‘Resolve’ may be concurrent at the expense of some complexity in tile buffer management (or simply double buffering the tile buffer).
LRZ explained in next Slide.

## Slide 7: Power advantages of tiled rendering
Chart: Direct vs. Binning: Power consumption
| Direct | Binning
 | 1 | 0.80014
Note:
Application – GFXBench Manhattan 3.0
Measured on Snapdragon silicon
  The binning pass can generate an low-resolution Z buffer, which is then used in later passes. Similar to a depth pre pass, this provides a level of Hidden-Surface-Removal even for late occludes. This is typically kept in system semory as it is very low bandwidth
  Memory bandwidth is obviously saved during fragment shading as only a single write per pixel is done. For MSAA, any sample filtering is done purely on-chip.
  While vertex bandwidth and processing may appear to increase relative to direct rendering, this is not really so as:
    Only the position information is required during the binning pass. The visibility information produced requires minimal bandwidth.
    During the render passes – any back-facing or LRZ occlude vertex is not fetched. So in many cases, the non-position bandwidth associated with a vertex is totally saved.
    Qualcomm, at least, uses fairly large tile buffers (512KB or more). Most primitives hit in only a single tile, limiting any vertex over fetch.
  ‘Vulkan Subpass’ usage can allow data to stay in the tile buffer for re-use on a later sub-pass.
Notes: Roughly 20% in this app – but can vary widely (hence the need for ‘Flex Render’)

## Slide 8: Comparison of mobile vs traditional laptop GPUs
Performance:
  Traditional Laptop GPUs still show a significant performance over mobile parts in the laptop environment.
  The delta is larger when comparing peak performance in traditional laptops with higher end SoCs and discrete graphics cards.
Power efficiency (Perf/Watt), is just the opposite with mobile based parts showing >2x advantage.
Chart: Graphics Performance and Power efficiency on detachable laptop (5W TDP)
| Performance | Power efficiency
Snapdragon Laptop | 0.68027 | 2.381
Traditional Laptop | 1 | 1
Note:
Benchmark: DX11 based GFXbench Manhattan 3.0
Traditional laptop: HP Enxy X2 (Kaby Lake – core i5 7Y54)
Snapdragon laptop: HP Envy X2 (SDM835)
Notes: Would have liked to get Desktop part comparison as well – but it is difficult to get a true apples to apples comparison. HP envy X2 happens to be a device available in both forms.
This is pessimistic to Qualcomm parts – as our drivers are very mobile/android focused and haven’t yet been full optimized for Windows

## Slide 9: Physical design and power management approaches for mobile
Exploiting fast transitions
2-5% perf gain across use cases
Ack: Edwin Jose
Fast DCVS Transitions
Exploiting fast DCVS transitions for sub-frame Clk/Voltage selection with workload awareness
DCVS during GPU binning phase
Low peak current region of frame run at higher FMAX
Aggressive Dynamic Clock and Voltage Scaling (DCVS) managed by local power management processor
Extensive clock tree gating with analysis tools to point out ungated clock trees.
Dedicated data paths and bypasses for different instructions.
  Despite a MUL-ADD pipeline, an A+B is not executed as 1.0*A+B
  Often data values of 0 or 1 are detected to trigger a ‘bypass’ path to avoid lighting up a multiplier or adder.
A key solution to achieve lower power consumption and yet fulfil the need for higher performance is by going ‘wide and slow’ with lower clocks and voltages
Leakage is constrained by trading off frequency and avoiding low Vt device selection
Notes: Dedicated ARM processor that monitors GPU activity. Not the Command Processor. Raise clock frequency in low power consumption times to improve overall perf..

## Slide 10: Future Challenges
While aggressive cooling technologies could help, the overall heat dissipation envelope needed for a handheld device is unlikely to change. Hence 6W to 8W is still the absolute mobile limit.
Mobile GPUs are nearing the limitations of the ‘wide and slow’ approach as we hit the minimum voltage levels for a given process.
Moore’s Law is slowing down. Process improvements are minimal moving forward.
Some possible solutions:
  More Power Efficient Memory Systems. ‘HBM’ (High Bandwidth Memory) where memory and GPU are interconnected via silicon and thru-silicon-via.
  New rendering techniques that inherently render less (such as VRS).
  Continued Compression improvements`
Notes: Currently have chips in 7nm with plans for 5nm – but the perf/watt benefits are diminishing with each generation.
Going absolute lowest voltage is tricky – and depends on accurate tools. If we go too low -- slowing down the clock doesn’t compensate as the transistor simply doesn’t work.